## Slide 1
CSE 140L
Combinational ALU
Arvind
Computer Science & Artificial Intelligence Lab.
Massachusetts Institute of Technology
Visiting Scholar UCSD
January 23, 2017

## Slide 2: Outline
Building complex combinational circuits in pieces
Parameterization that goes beyond data path widths

## Slide 3: Arithmetic-Logic Unit (ALU)
func
- Add, Sub, And, Or, ...
result
a
b
ALU
what does func look like?
function Data alu(Data a, Data b,
AluFunc func);
ALU performs all the arithmetic and logical functions
Each individual function can be described as a combinational circuit and these can be combined together to produce a combinational ALU
Type of a, e.g., Bit#(32)
Notes: Data could be bit#(32)

## Slide 4: ALU for comparison operators
func
- GT, LT, EQ, Zero, ...
c
a
b
ALU Br
what does func look like?
function Bool aluBr(Data a, Data b,
BrFunc func);
Like ALU but returns a Bool
Notes: Data could be bit#(32)

## Slide 5: Enumerated types
Suppose we have a variable c whose values can represent three different colors
  Declare the type of c to be Bit#(2) and adopt the convention that 00 represents Red, 01 Blue and 10 Green
A better way is to create a new type called Color:
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
BSV compiler automatically assigns a bit representation to the three colors and provides a function to test if the two colors are equal
Types prevent us from mixing colors with raw bits
Why is this way better?
If you do not use “deriving” then you will have to specify your encoding and equality function

## Slide 6: Enumerated types
typedef enum {Red, Blue, Green}
Color deriving(Bits, Eq);
typedef enum {Add, Sub, And, Or, Xor, Nor, Slt, Sltu, LShift, RShift, Sra} AluFunc deriving(Bits, Eq);
typedef enum {Eq, Neq, Le, Lt, Ge, Gt, AT, NT}
BrFunc deriving(Bits, Eq);
Each enumerated type defines a new type

## Slide 7: Combinational ALU
function Data alu(Data a, Data b, AluFunc func);
Data res = case(func)
Add : addN(a,b);
Sub : subN(a,b);
And : andN(a,b);
Or : orN(a,b);
Xor : xorN(a,b);
Nor : norN(a,b);
Slt : zeroExtend(pack(signedLT(a,b)));
Sltu : zeroExtend(pack(lt(a,b));
LShift: shiftLeft(a,b[4:0]);
RShift: shiftRight(a,b[4:0]);
Sra : signedShiftRight(a,b[4:0]);
endcase;
return res;
endfunction
Given an implementation of the primitive operations like addN, Shift, etc. the ALU can be implemented simply by introducing a mux controlled by func to select the appropriate circuit
Notes: Slt, Sltu?

## Slide 8: Comparison operators
function Bool aluBr(Data a, Data b, BrFunc brFunc);
Bool brTaken = case(brFunc)
Eq : (a == b);
Neq : (a != b);
Le : signedLE(a,b);
Lt : signedLT(a,b);
Ge : signedGE(a,b);
Gt : signedGT(a,b);
AT : True;
NT : False;
endcase;
return brTaken;
endfunction
Notes: 8
We only compare with 0?

## Slide 9: ALU including Comparison operators
mux
a
func
…
mux
brFunc
Add
LShift
Eq
…
b

## Slide 10: Shift operators

## Slide 11: Logical right shift by 2
Fixed size shift operation is cheap in hardware – just wire the circuit appropriately
Other types of shifts are similar
0
0
a b c d
0 0 a b
a b c d
c d a b
Rotate
a b c d
a a a b
Sign-
extended
Sign extension is useful for converting say, a 32-bit integer into a 64-bit integer

## Slide 12: Logical right shift by n
Shift n can be broken down in log n steps of fixed-length shifts of size 1, 2, 4, …. For example, we can perform
  Shift 3 (=2+1) by doing shifts of size 2 and 1
  Shift 5 (=4+1) by doing shifts of size
  Shift 21 (=16+4+1) by doings shifts of size
For a 32-bit number, a 5-bit n can specify all the needed shifts
  310 = 000112 , 510 = 001012 , 2110 = 101012
The bit encoding of n tells us which shifters are needed; if the value of the ith (least significant) bit is 1 then we need to shift by 2i bits
4 and 1
16, 4 and 1

## Slide 13: Conditional operation: shift versus no-shift
We need a mux to select the appropriate wires: if s is one the mux will select the wires on the left otherwise it would select wires on the right
s
(s==0)?{a,b,c,d}:{0,0,a,b};
0
0

## Slide 14: Logical right shift ckt
Define log n shifters of sizes 1, 2, 4, …
Define log n muxes to perform a particular size shift
Shift circuit can be expressed as log n nested conditional expressions where s0, s1 .. Represent the bits of n
0
0
0
s0
s1
In Lab 3 you would design such a shifter

## Slide 15: Complex Combinational Circuits

## Slide 16: Multiplication by repeated addition
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
mi = (a[i]==0)? 0 : b;
At each step we add either 1101 or 0 to the result depending upon a bit in the multiplier
We also shift the result by one position at every step
Notice, the first addition is unnecessary because it simply yields m0

## Slide 17: Multiplication by repeated addition ckt
1101 (13)
1011 (11)
0000
+ 1101
01101
+ 1101
100111
+ 0000
0100111
+ 1101
10001111 (143)
b Multiplicand
a Muliplier *
tp
m0
tp
m1
tp
m2
tp
m3
tp
mi = (a[i]==0)? 0 : b;
add4
a1
m1
a2
m2
a3
m3
add4
add4
0
a0
m0

## Slide 18: Combinational 32-bit multiply
function Bit#(64) mul32(Bit#(32) a, Bit#(32) b);
Bit#(32) tp = 0; Bit#(32) prod = 0; for(Integer i = 0; i < 32; i = i+1) begin Bit#(32) m = (a[i]==0)? 0 : b; Bit#(33) sum = add32(m,tp,0); prod[i] = sum[0];
tp = sum[32:1];
end return {tp,prod}; endfunction
Lot of gates!
This circuit uses 31 add32 circuits
Long chains of gates
  32-bit multiply has 31 ripple carry adders in sequence!
  32-bit ripple carry adder has a 31-long chain of gates
  Total delay ?
  2(n-1) FAs?
  2(n-1) FAs?
Can we do better?
Stay tuned…